## Slide 1
PowerPoint Slides
Smruti Ranjan Sarangi, IIT Delhi
Chapter 3- Assembly Language
PROPRIETARY MATERIAL. © 2014 The McGraw-Hill Companies, Inc. All rights reserved. No part of this PowerPoint slide may be displayed, reproduced or distributed in any form or by any means, without the prior written permission of the publisher, or used beyond the limited distribution to teachers and educators permitted by McGraw-Hill for their individual course preparation. PowerPoint Slides are being provided only to authorized professors and instructors for use in preparing for classes using the affiliated textbook. No other use or distribution of this PowerPoint slide is permitted. The PowerPoint slide may not be sold and may not be distributed or be used by any student or any other third party. No part of the slide may be reproduced, displayed or distributed in any form or by any means, electronic or otherwise, without the prior written permission of McGraw Hill Education (India) Private Limited.
Computer Organisation and Architecture

## Slide 2
Download the pdf of the book
www.basiccomparch.com
videos
Slides, software, solution manual
Print version
(Publisher: WhiteFalcon, 2021)
Available on e-commerce sites.
The pdf version of the book and all the learning resources can be freely downloaded from the website: www.basiccomparch.com
2nd version

## Slide 3: Outline
Overview of Assembly Language
Assembly Language Syntax
SimpleRisc ISA
Functions and Stacks
SimpleRisc Encoding

## Slide 4: What is Assembly Language
  A low level programming language uses simple statements that correspond to typically just one machine instruction. These languages are specific to the ISA.
  The term “assembly language” refers to a family of low-level programming languages that are specific to an ISA. They have a generic structure that consists of a sequence of assembly statements.
  Typically, each assembly statement has two parts: (1) an instruction code that is a mnemonic for a basic machine instruction, and (2) and a list of operands.

## Slide 5: Why learn Assembly Language ?
Software developers' perspective
  Write highly efficient code
    Suitable for the core parts of games, and mission critical software
  Write code for operating systems and device drivers
  Use features of the machine that are not supported by standard programming languages

## Slide 6: Assemblers
Assemblers are programs that convert programs written in low level languages to machine code (0s and 1s)
Examples :
  nasm, tasm, and masm for x86 ISAs
  On a linux system try :
    gcc -S <filename.c>
    filename.s is its assembly representation
    Then type: gcc filename.s (will generate a binary: a.out)

## Slide 7: Hardware Designers Perspective
Learning the assembly language is the same as learning the intricacies of the instruction set
Tells HW designers : what to build ?

## Slide 8: Machine Model – Von Neumann Machine with Registers
CPU
Control
ALU
Memory
I/O devices
Registers

## Slide 9: View of Registers
Registers → named storage locations
  in ARM : r0, r1, … r15
  in x86 : eax, ebx, ecx, edx, esi, edi
Machine specific registers (MSR)
  Examples : Control the machine such as the speed of fans, power control settings
  Read the on-chip temperature.
Registers with special functions :
  stack pointer
  program counter
  return address

## Slide 10: View of Memory
Memory
  One large array of bytes
  Each location has an address
  The address of the first location is 0, and increases by 1 for each subsequent location
The program is stored in a part of the memory
The program counter contains the address of the current instruction

## Slide 11: Storage of Data in Memory
Data Types
  char (1 byte), short (2 bytes), int (4 bytes), long int (8 bytes)
How are multibyte variables stored in memory ?
  Example : How is a 4 byte integer stored ?
  Save the 4 bytes in consecutive locations
  Little endian representation (used in ARM and x86) → The LSB is stored in the lowest location
  Big endian representation (Sun Sparc, IBM PPC) → The MSB is stored in the lowest location

## Slide 12: Little Endian vs Big Endian
Note the order of the storage of bytes
8
7
6
5
4
3
21
21 43 65 87
0x87654321
Big endian
Little endian
0 1 2 3
0 1 2 3

## Slide 13: Storage of Arrays in Memory
Single dimensional arrays. Consider an array of integers : a[100]
Each integer is stored in either a little endian or big endian format
2 dimensional arrays :
  int a[100][100]
  float b[100][100]
  Two methods : row major and column major
a[0]
a[1]
a[2]

## Slide 14: Row Major vs Column Major
Row Major (C, Python)
  Store the first row as an 1D array
  Then store the second row, and so on...
Column Major (Fortran, Matlab)
  Store the first column as an 1D array
  Then store the second column, and so on
Multidimensional arrays
  Store the entire array as a sequence of 1D arrays

## Slide 15: Outline
Overview of Assembly Language
Assembly Language Syntax
SimpleRisc ISA
Functions and Stacks
SimpleRisc Encoding

## Slide 16: Assembly File Structure : GNU Assembler
Divided into different sections
Each section contains some data, or assembly instructions
.file
.text
.data
Assembly File

## Slide 17: Meaning of Different Sections
.file
  name of the source file
.text
  contains the list of instructions
.data
  data used by the program in terms of read only variables, and constants

## Slide 18: Structure of a Statement
instruction
  textual identifier of a machine instruction
operand
  constant (also known as an immediate)
  register
  memory location
Instruction
operand 1
operand n
operand 2

## Slide 19: Examples of Instructions
subtract the contents of r2 from the contents of r1, and save the result in r3
multiply the contents of r2 with the contents of r1, and save the results in r3
sub r3, r1, r2
mul r3, r1, r2

## Slide 20: Generic Statement Structure
label → identifier of a statement
directive → tells the assembler to do something like declare a function
constant → declares a constant
Label
:
Directive
Constant
Assembly
instruction
Comment
@
Comment
/*
*/

## Slide 21: Generic Statement Structure - II
assembly statement → contains the assembly instruction, and operands
comment → textual annotations ignored by the assembler
Label
:
Directive
Constant
Assembly
instruction
Comment
@
Comment
/*
*/

## Slide 22: Types of Instructions
Data Processing Instructions
  add, subtract, multiply, divide, compare, logical or, logical and
Data Transfer Instructions
  transfer values between registers, and memory locations
Branch instructions
  branch to a given label
Special instructions
  interact with peripheral devices, and other programs, set machine specific parameters

## Slide 23: Nature of Operands
Classification of instructions
  If an instruction takes n operands, then it is said to be in the n-address format
  Example : add r1, r2, r3 (3 address format)
Addressing Mode
  The method of specifying and accessing an operand in an assembly statement is known as the addressing mode.

## Slide 24: Register Transfer Notation
This notation allows us to specify the semantics of instructions
r1 ← r2
  transfer the contents of register r2 to register r1
r1 ← r2 + 4
  add 4 to the contents of register r2, and transfer the contents to register r1
r1 ← [r2]
  access the memory location that matches the contents of r2, and store the data in register r1

## Slide 25: Addressing Modes
Let V be the value of an operand, and let r1, r2 specify registers
Immediate addressing mode
  V ← imm , e.g. 4, 8, 0x13, -3
Register direct addressing mode
  V ← r1
  e.g. r1, r2, r3 …
Register indirect
  V ← [r1]
Base-offset : V ← [r1 + offset], e.g. 20[r1] (V ← [20+r1])

## Slide 26: Register Indirect Mode
V ← [r1]
r1
register file
memory
value

## Slide 27: Base-offset Addressing Mode
V ← [r1+offset]
r1
register file
memory
value
offset

## Slide 28: Addressing Modes - II
Base-index-offset
  V ← [r1 + r2 + offset]
  example: 100[r1,r2] (V ← [r1 + r2 + 100])
Memory Direct
  V ← [addr]
  example : [0x12ABCD03]
PC Relative
  V ← [pc + offset]
  example: 100[pc] (V ← [pc + 100])

## Slide 29: Base-Index-Offset Addressing Mode
V ← [r1+r2 +offset]
r1
register file
memory
value
offset
r2

## Slide 30: Outline
Overview of Assembly Language
Assembly Language Syntax
SimpleRisc ISA
Functions and Stacks
SimpleRisc Encoding

## Slide 31: SimpleRisc
Simple RISC ISA
Contains only 21 instructions
We will design an assembly language for SimpleRisc
Design a simple binary encoding,
and then implement it ...

## Slide 32: Survey of Instruction Sets
ISA
Type
Year
Vendor
Bits
Endianness
Registers
VAX
CISC
1977
DEC
32
little
16
SPARC
RISC
1986
Sun
32
big
32
RISC
1993
Sun
64
bi
32
PowerPC
RISC
1992
Apple,IBM,Motorola
32
bi
32
RISC
2002
Apple,IBM
64
bi
32
PA-RISC
RISC
1986
HP
32
big
32
RISC
1996
HP
64
big
32
m68000
CISC
1979
Motorola
16
big
16
CISC
1979
Motorola
32
big
16
MIPS
RISC
1981
MIPS
32
bi
32
RISC
1999
MIPS
64
bi
32
Alpha
RISC
1992
DEC
64
bi
32
x86
CISC
1978
Intel,AMD
16
little
8
CISC
1985
Intel,AMD
32
little
8
CISC
2003
Intel,AMD
64
little
16
ARM
RISC
1985
ARM
32
bi(little default)
16
RISC
2011
ARM
64
bi(little default)
31

## Slide 33: Registers
SimpleRisc has 16 registers
  Numbered : r0 … r15
  r14 is also referred to as the stack pointer (sp)
  r15 is also referred to as the return address register (ra)
View of Memory
  Von Neumann model
  One large array of bytes
Special flags register → contains the result of the last comparison
  flags.E = 1 (equality), flags.GT = 1 (greater than)

## Slide 34: mov instruction
Transfer the contents of one register to another
Or, transfer the contents of an immediate to a register
The value of the immediate is embedded in the instruction
  SimpleRisc has 16 bit immediates
  Range -215 to 215 - 1
mov r1,r2
r
1
¬
r
2
mov r1,3
r
1
¬
3

## Slide 35: Arithmetic/Logical Instructions
SimpleRisc has 6 arithmetic instructions
  add, sub, mul, div, mod, cmp
Example
Explanation
add r1, r2, r3
add r1, r2, 10
sub r1, r2, r3
mul r1, r2, r3
div r1, r2, r3
mod r1, r2, r3
cmp r1, r2
r1 r2 + r3
¬
r1 r2 + 10
¬
r1 r2 – r3
¬
r1 r2 × r3
¬
r1 r2/r3 (quotient)
¬
r1 r2 mod r3 (remainder)
¬
set flags

## Slide 36: Examples of Arithmetic Instructions
Convert the following code to assembly
Assign the variables to registers
  a ← r0, b ← r1, c ← r2, d ← r3
a = 3
b = 5
c = a + b
d = c - 5
mov r0, 3
mov r1, 5
add r2, r0, r1
sub r3, r2, 5

## Slide 37: Examples - II
Convert the following code to assembly
Assign the variables to registers
  a ← r0, b ← r1, c ← r2, d ← r3
a = 3
b = 5
c = a * b
d = c mod 5
mov r0, 3
mov r1, 5
mul r2, r0, r1
mod r3, r2, 5

## Slide 38: Compare Instruction
Compare 3 and 5, and print the value of the flags
flags.E = 0, flags.GT = 0
a = 3
b = 5
compare a and b
mov r0, 3
mov r1, 5
cmp r0, r1

## Slide 39
Compare 5 and 3, and print the value of the flags
flags.E = 0, flags.GT = 1
a = 5
b = 3
compare a and b
mov r0, 5
mov r1, 3
cmp r0, r1
Compare Instruction

## Slide 40: Compare Instruction
Compare 5 and 5, and print the value of the flags
flags.E = 1, flags.GT = 0
a = 5
b = 5
compare a and b
mov r0, 5
mov r1, 5
cmp r0, r1

## Slide 41: Example with Division
Write assembly code in SimpleRisc to compute: 31 / 29 - 50, and save the
result in r4.
Answer:
SimpleRisc
mov r1, 31
mov r2, 29
div r3, r1, r2
sub r4, r3, 50

## Slide 42: Logical Instructions
The second argument can either be a register or an immediate
and r1, r2, r3
r1  r2 & r3
or r1, r2, r3
not r1, r2
r1  r2 | r3
r1  ~ r2
& bitwise AND, | bitwise OR, ~ logical complement
Compute (a | b). Assume that a is stored in r0, and b is stored in r1. Store
the result in r2.
Answer:
SimpleRisc
or r2, r0, r1

## Slide 43: Shift Instructions
Logical shift left (lsl) (<< operator)
  0010 << 2 is equal to 1000
  (<< n) is the same as multiplying by 2n
Arithmetic shift right (asr) (>> operator)
  0010 >> 1 = 0001
  1000 >> 2 = 1110
  same as dividing a signed number by 2n

## Slide 44: Shift Instructions - II
logical shift right (lsr) (>>> operator)
  1000 >>> 2 = 0010
  same as dividing the unsigned representation by 2n
Example
Explanation
lsl r3, r1, r2
r3  r1 << r2 (shift left)
lsl r3, r1, 4
lsr r3, r1, r2
lsr r3, r1, 4
asr r3, r1, r2
asr r3, r1, 4
r3  r1 << 4 (shift left)
r3  r1 >>> r2 (shift right logical)
r3  r1 >>> 4 (shift right logical)
r3  r1 >> r2 (arithmetic shift right)
r3  r1 >> r2 (arithmetic shift right)

## Slide 45: Example with Shift Instructions
Compute 101 * 6 with shift operators
mov r0, 101
lsl r1, r0, 1
lsl r2, r0, 2
add r3, r1, r2

## Slide 46: Example - II
Compute 102 * 7.5 with shift operators
mov r0, 102
lsl r1, r0, 3
lsr r2, r0, 1
sub r3, r1, r2

## Slide 47: Load-store instructions
2 address format, base-offset addressing
Fetch the contents of r2, add the offset (10), and then perform the memory access
ld r1, 10[r2]
r1  [r2 +10]
st r1, 10[r2]
[r2+10] 
r1

## Slide 48: Load-Store
ld r1, 10[r2]
r1
r2
register
file
memory
10
st r1, 10[r2]
r1
r2
register
file
memory
10
(a)
(b)

## Slide 49: Example – Load/Store
Translate :
int arr[10];
arr[3] = 5;
arr[4] = 8;
arr[5] = arr[4] + arr[3];
/* assume base of array saved in r0 */
mov r1, 5
st r1, 12[r0]
mov r2, 8
st r2, 16[r0]
add r3, r1, r2
st r3, 20[r0]

## Slide 50: Branch Instructions
Unconditional branch instruction
b .foo
branch to .foo
add r1, r2, r3
b .foo
...
...
.foo:
add r3, r1, r4

## Slide 51: Conditional Branch Instructions
The flags are only set by cmp instructions
beq (branch if equal)
  If flags.E = 1, jump to .foo
bgt (branch if greater than)
  If flags.GT = 1, jump to .foo
beq .foo
branch to .foo if flags.E = 1
bgt .foo
branch to .foo if flags.GT = 1

## Slide 52: Examples
If r1 > r2, then save 4 in r3, else save 5 in r3
cmp r1, r2
bgt .gtlabel
mov r3, 5
...
...
.gtlabel:
mov r3, 4

## Slide 53: Example - II
C
SimpleRisc
int prod = 1;
int idx;
for(idx = num; idx > 1; idx --) {
prod = prod * idx
}
mov r1, 1 /* prod = 1 */
mov r2, r0 /* idx = num */
.loop:
mul r1, r1, r2 /* prod = prod * idx */
sub r2, r2, 1 /* idx = idx - 1 */
cmp r2, 1 /* compare (idx, 1) */
bgt .loop /* if (idx > 1) goto .loop*/
Let us now try to convert this program to SimpleRisc .
Answer: Compute the factorial of the variable num.

## Slide 54
Write a SimpleRisc assembly program to find the smallest number that is a sum of two cubes in two different ways → 1729

## Slide 55: Modifiers
We can add the following modifiers to an instruction that has an immediate operand
Modifier :
  default : mov → treat the 16 bit immediate as a signed number (automatic sign extension)
  (u) : movu → treat the 16 bit immediate as an unsigned number
  (h) : movh → left shift the 16 bit immediate by 16 positions

## Slide 56: Mechanism
The processor internally converts a 16 bit immediate to a 32 bit number
It uses this 32 bit number for all the computations
Valid only for arithmetic/logical insts
We can control the generation of this 32 bit number
  sign extension (default)
  treat the 16 bit number as unsigned (u suffix)
  load the 16 bit number in the upper bytes (h suffix)

## Slide 57: More about Modifiers
default : mov r1, 0xAB 12
unsigned : movu r1, 0xAB 12
high: movh r1, 0xAB 12
AB
12
sign bit
00
00
AB
12
AB
12
00
00

## Slide 58: Examples
Move : 0x FF FF A3 2B in r0
Move : 0x 00 00 A3 2B in r0
Move : 0x A3 2B 00 00 in r0
mov r0, 0xA32B
movu r0, 0xA32B
movh r0, 0xA32B

## Slide 59
Set r0 ← 0x 12 AB A9 2D
movh r0, 0x 12 AB
addu r0, 0x A9 2D
Example

## Slide 60: Outline
Overview of Assembly Language
Assembly Language Syntax
SimpleRisc ISA
Functions and Stacks
SimpleRisc Encoding

## Slide 61: Implementing Functions
Functions are blocks of assembly instructions that can be repeatedly invoked to perform a certain action
Every function has a starting address in memory (e.g. foo has a starting address A
function foo
A

## Slide 62: Implementing Functions - II
To call a function, we need to set :
  pc ← A
We also need to store the location of the pc that we need to come to after the function returns
This is known as the return address
We can thus call any function, execute its instructions, and then return to the saved return address

## Slide 63: Notion of the Return Address
PC of the call instruction → p
PC of the return address → p + 4
because, every instruction takes 4 bytes
function call
ret
return address
caller
callee
p
p+4

## Slide 64: How do we pass arguments/ return values
Solution : use registers
SimpleRisc
.foo:
add r2, r0, r1
ret
.main:
mov r0, 3
mov r1, 5
call .foo
add r3, r2, 10

## Slide 65: Problems with this Mechanism
Space Problem
  We have a limited number of registers
  We cannot pass more than 16 arguments
  Solution : Use memory also
Overwrite Problem
  What if a function calls itself ? (recursive call)
  The callee can overwrite the registers of the caller
  Solution : Spilling

## Slide 66: Register Spilling
The notion of spilling
  The caller can save the set of registers its needs
  Call the function
  And then restore the set of registers after the function returns
  Known as the caller saved scheme
callee saved scheme
  The callee saves, the registers, and later restores them

## Slide 67: Spilling
Save registers
Restore registers
Callee
Caller
Save registers
Restore registers
Callee
Caller
(a)
(b)
Caller saved
Callee saved

## Slide 68: Problems with our Approach
Using memory, and spilling solves both the space problem and overwrite problem
However, there needs to be :
  a strict agreement between the caller and the callee regarding the set of memory locations that need to be used
  Secondly, after a function has finished execution, all the space that it uses needs to be reclaimed

## Slide 69: Activation Block
Activation block → memory map of a function
arguments, register spill area, local vars
int foo(int arg1) {
int a, b, c;
a = 3; b = 4;
c = a + b + arg1;
return c;
}
Activation block
Arguments
Return address
Register spill area
Local variables

## Slide 70: How to use activation blocks ?
Assume caller saved spilling
Before calling a function : spill the registers
Allocate the activation block of the callee
Write the arguments to the activation block of the callee, if they do not fit in registers
Call the function

## Slide 71: Using Activation Blocks - II
In the called function
  Read the arguments and transfer to registers (if required)
  Save the return address if the called function can call other functions
  Allocate space for local variables
  Execute the function
Once the function ends
  Restore the value of the return address register (if required)
  Write the return values to registers, or the activation block of the caller
  Destroy the activation block of the callee

## Slide 72: Using Activation Blocks - III
Once the function ends (contd …)
  Call the ret instruction
  and return to the caller
The caller :
  Retrieve the return values from the registers of from its activation block
  Restore the spilled registers
  continue ...

## Slide 73: Organising Activation Blocks
All the information of an executing function is stored in its activation block
These blocks need to be dynamically created and destroyed – millions of times
What is the correct way of managing them, and ensuring their fast creation and deletion ?
Is there a pattern ?

## Slide 74: Pattern of Function Calls
foo
main
test
test2
foobar
foobarbar
main() {
test();
foo();
}
test() {
...
test2();
return;
}
test2() {
...
return;
}
foo() {
...
foobar();
return;
}
foobar() {
...
foobarbar();
return;
}
foobarbar() {
...
return;
}

## Slide 75: Pattern of Function Calls
Last in First Out
Use a stack to store activation blocks
Stack
foo
foo
foobar
foo
foobar
foobarbar
foo
foobar
(a)
(b)
(c)
(d)

## Slide 76: Working with the Stack
Allocate a part of the memory to save the stack
Traditionally stacks are downward growing.
  The first activation block starts at the highest address
  Subsequent activation blocks are allocated lower addresses
The stack pointer register (sp (14)) points to the beginning of an activation block
Allocating an activation block :
  sp ← sp - <constant>
De-allocating an activation block :
  sp ← sp + <constant>

## Slide 77: What has the Stack Solved ?
Space problem
  Pass as many parameters as required in the activation block
Overwrite problem
  Solved by activation blocks
Management of activation blocks
  Solved by the notion of the stack
The stack needs to primarily be managed in software

## Slide 78: call and ret instructions
ra (or r15)  return address register
call instruction
  Puts pc + 4 in ra, and jumps to the function
ret instruction
  Puts ra in pc
call .foo
ret
ra ← PC + 4 ; PC ← address(.foo);
PC ← ra

## Slide 79: Recursive Factorial Program
C
int factorial(int num) {
if (num <= 1) return 1;
return num * factorial(num - 1);
}
void main() {
int result = factorial(10);
}

## Slide 80: Factorial in SimpleRisc
.factorial:
cmp r0, 1 /* compare (1,num) */
beq .return
bgt .continue
b .return
.continue:
sub sp, sp, 8 /* create space on the stack */
st r0, [sp] /* push r0 on the stack */
st ra, 4[sp] /* push the return address register */
sub r0, r0, 1 /* num = num - 1 */
call .factorial /* result will be in r1 */
ld r0, [sp] /* pop r0 from the stack */
ld ra, 4[sp] /* restore the return address */
mul r1, r0, r1 /* factorial(n) = n * factorial(n-1) */
add sp, sp, 8 /* delete the activation block */
ret
.return:
mov r1, 1
ret
.main:
mov r0, 10
call .factorial

## Slide 81: nop instruction
nop → does nothing
Example : nop

## Slide 82: Outline
Overview of Assembly Language
Assembly Language Syntax
SimpleRisc ISA
Functions and Stacks
SimpleRisc Encoding

## Slide 83: Encoding Instructions
Encode the SimpleRisc ISA using 32 bits.
We have 21 instructions. Let us allot each instruction an unique code (opcode)
Instruction
Code
Instruction
Code
Instruction
Code
add
00000
not
01000
beq
10000
sub
00001
mov
01001
bgt
10001
mul
00010
lsl
01010
b
10010
div
00011
lsr
01011
call
10011
mod
00100
asr
01100
ret
10100
cmp
00101
nop
01101
and
00110
ld
01110
or
00111
st
01111

## Slide 84: Basic Instruction Format
opcode
rest of the instruction
5
27
Inst.
Code
Format
Inst.
Code
Format
add
00000
add rd,
rs1
, (rs2/imm)
lsl
01010
l
s
l
rd
,
rs
1
, (rs2/i
mm
)
sub
00001
sub rd,
rs1
, (rs2/i
mm)
lsr
01011
lsr rd, rs1
, (rs2/imm)
mul
00010
m
u
l
rd,
rs1
, (rs2/imm)
asr
01100
asr rd, rs1
, (rs2/imm)
div
00011
di
v rd,
rs1
, (rs2/imm)
nop
01101
nop
mod
00100
mod
rd,
rs1
, (rs2/i
mm
)
ld
01110
ld
rd.
imm
[rs
1
]
cmp
00101
cmp
rs1
, (rs2/imm)
st
01111
st rd. imm
[rs1]
and
00110
and r
d
,
rs1
, (rs2/imm)
beq
10000
be
q offset
or
00111
or rd,
rs1
, (rs2/imm)
bgt
10001
bgt offset
not
01000
not rd, (rs2/imm)
b
10010
b offset
mov
01001
mov rd, (rs2/imm)
call
10011
call offset
ret
1010
0
ret

## Slide 85: 0-Address Instructions
nop and ret instructions
opcode
5
32

## Slide 86: 1-Address Instructions
Instructions – call, b, beq, bgt
Use the branch format
Fields :
  5 bit opcode
  27 bit offset (PC relative addressing)
  Since the offset points to a 4 byte word address
    The actual address computed is : PC + offset * 4
opcode
5
32
offset
27
op
offset

## Slide 87: 3-Address Instructions
Instructions – add, sub, mul, div, mod, and, or, lsl, lsr, asr
Generic 3 address instruction
  <opcode> rd, rs1, <rs2/imm>
Let us use the I bit to specify if the second operand is an immediate or a register.
  I = 0 → second operand is a register
  I = 1 → second operand is an immediate
Since we have 16 registers, we need 4 bits to specify a register

## Slide 88: Register Format
opcode → type of the instruction
I bit → 0 (second operand is a register)
dest reg → rd
source register 1 → rs1
source register 2 → rs2
opcode
5
32
0
dest reg
src reg1
src reg2
4
4
4
op
I
1
rd
rs1
rs2

## Slide 89: Immediate Format
opcode → type of the instruction
I bit → 1 (second operand is an immediate)
dest reg → rd
source register 1 → rs1
Immediate → imm
modifier bits → 00 (default), 01 (u), 10 (h)
opcode
32
1
dest reg
src reg1
immediate
18
5
4
4
op
I
1
rd
rs1
imm
2
modifier bits

## Slide 90: 2 Address Instructions
cmp, not, and mov
Use the 3 address : immediate or register formats
Do not use one of the fields

## Slide 91: cmp, not, and mov
00101
5
32
rs1
4
4
rs2 / imm
18
cmp
01001
5
32
rd
4
4
rs2 / imm
18
mov
01000
5
32
4
4
rs2/ imm
18
not
I
I
I
rd
1
1
1

## Slide 92: Load and Store Instructions
ld rd, imm[rs1]
rs1 → base register
Use the immediate format.
01110
5
32
rs1
4
4
18
ld rd, imm[rs1]
1
1
rd
imm

## Slide 93: Store Instruction
Strange case of the store inst.
st reg1, imm[reg2]
has two register sources, no register destination, 1 immediate
Cannot fit in the immediate format, because the second operand can be either be a register OR an immediate (not both)
        Should we define a new format for store instructions ?
Maybe not

## Slide 94: Store Instruction
Let us make an exception and use the immediate format.
We use the rd field to save one of the source registers
st rd, imm[rs1]
01111
5
32
rs1
4
4
18
st rd, imm[rs1]
1
1
rd
imm

## Slide 95: Summary of Instruction Formats
branch format → nop, ret, call, b, beq, bgt
register format → ALU instructions
immediate format → ALU, ld/st instructions
Format
Definition
branch
op
(28-32)
offset
(1-27)
register
op
(28-32)
I
(27)
rd
(23-26)
rs
1(19-22)
rs
2(15-18)
immediate
op
(28-32)
I
(27)
rd
(23-26)
rs
1(19-22)
imm
(1-18)
op → opcode, offset → branch offset, I → immediate bit, rd → destination register
rs1 → source register 1, rs2 → source register 2, imm → immediate operand

## Slide 96
THE END