## Slide 1
Chapter 6 A Primer On Digital Logic
Power Point Slides
PROPRIETARY MATERIAL. © 2014 The McGraw-Hill Companies, Inc. All rights reserved. No part of this PowerPoint slide may be displayed, reproduced or distributed in any form or by any means, without the prior written permission of the publisher, or used beyond the limited distribution to teachers and educators permitted by McGraw-Hill for their individual course preparation. PowerPoint Slides are being provided only to authorized professors and instructors for use in preparing for classes using the affiliated textbook. No other use or distribution of this PowerPoint slide is permitted. The PowerPoint slide may not be sold and may not be distributed or be used by any student or any other third party. No part of the slide may be reproduced, displayed or distributed in any form or by any means, electronic or otherwise, without the prior written permission of McGraw Hill Education (India) Private Limited.
1
Smruti Ranjan Sarangi, IIT Delhi
Computer Organisation and Architecture

## Slide 2
Download the pdf of the book
www.basiccomparch.com
videos
Slides, software, solution manual
Print version
(Publisher: WhiteFalcon, 2021)
Available on e-commerce sites.
The pdf version of the book and all the learning resources can be freely downloaded from the website: www.basiccomparch.com
2nd version

## Slide 3
Outline
Transistors and Gates
Combinational Logic
Sequential Logic
SRAM/ DRAM Cells
3

## Slide 4
Disclaimer: This chapter is only to get a high level overview ...
We assume some background in logic gates, transistors, combinational and sequential logic
The aim of this chapter is to only provide a high level overview
For a deeper understanding consult any of the classic textbooks on digital logic

## Slide 5
Atoms and Molecules of Circuits
The Transistor
It is just a switch.
It is either switched on (current can flow), or switched off (no current flow)

## Slide 6
How is a Transistor Made?
It is made of Silicon
  Silicon is a semi-conductor.
  We can change its properties:
  Add a little bit of impurities  doping
Dope it with Group III elements
  Boron, Aluminum and Gallium
  It is called a p-type semiconductor
Or, dope it with Group V elements
  Phosphorus or Arsenic
  It is called a n-type semiconductor

## Slide 7
Silicon Lattice
This is a typical silicon lattice. Each Si atom is connected to 4 other atoms.
Si
Si
Si
Si
Si
Si
Si
Si
Si

## Slide 8
P-Type Doping
If there is a Boron atom in the lattice. It will create bonds with the rest of the atoms.
There will be one less electron (hole)
Holes can flow. They are associated with +ve charge. (see the animation)
Si
Si
Si
Si
B
Si
Si
Si
Si

## Slide 9
N-Type Doping
If there is a Phosphorus atom in the lattice. It will create bonds with the rest of the atoms.
There will be one more electron (electron)
Electrons can flow. They are associated with -ve charge. (see the animation)
Si
Si
Si
Si
P
Si
Si
Si
Si

## Slide 10
Let us make a transistor.
NMOS transistor  Put two n-type wells in a p-type substrate
Now, assume that we apply +ve charge to the gate.
Channel  This forms because electrons move towards the positive charge. Forms a conductive layer that can conduct current.
p-type
n-type
n-type
source
drain
gate
channel

## Slide 11
NMOS Transistor
Apply a +ve voltage
Current flows from the drain to source
drain
source
Apply a 0 or -ve voltage
No current flow.
We thus have a switch
  Apply a +ve voltage at the gate  make the transistor conduct
  Apply a –ve or 0 voltage at the gate  transistor is off (no current flow across it)
gate

## Slide 12
PMOS Transistor
PMOS transistor  Put two p-type wells in an n-type substrate
Now, assume we apply 0 or -ve charge to the gate.
Channel  This forms because holes move towards the gate. This channel can conduct current.
n-type
p-type
p-type
source
drain
gate
channel

## Slide 13
PMOS Transistor
Apply a 0 or -ve voltage
Current flows from the source to the drain
source
drain
Apply a +ve voltage
No current flow.
We thus have a switch
  Apply a +ve voltage at the gate  transistor is off (no current flow across it)
  Apply a –ve or 0 voltage at the gate transistor conducts
gate

## Slide 14
Let us make an inverter
A
A
Vcc
A
A
If A = 1 (+ve voltage)
T1 is on, T2 is off
Thus, the output will be connected to the ground, and it will be a logical 0
T1
T2
If A = 0 (0 voltage)
T1 is off, T2 is on
Thus, the output will be connected to the supply (Vcc), and it will be a logical 1

## Slide 15
NOR Gate
Vcc
T3
T2
A
B
A
B
T1
T4
A | B | T1 | T2 | T3 | T4 | Out
0 | 0 | off | off | on | on | 1
1 | 0 | on | off | off | on | 0
0 | 1 | off | on | on | off | 0
1 | 1 | on | on | off | off | 0
Out
B
A NOR B
A

## Slide 16
NAND Gate
Vcc
T3
T2
A
A
B
T1
T4
A | B | T1 | T2 | T3 | T4 | Out
0 | 0 | off | off | on | on | 1
1 | 0 | on | off | off | on | 1
0 | 1 | off | on | on | off | 1
1 | 1 | on | on | off | off | 0
Out
B
A
B
A NAND B

## Slide 17
Summary of Logic Gates
A
B
B
A OR B
A
A AND B
A
B
B
A NOR B
A NAND B
A
A
A

## Slide 18
Outline
Transistors and Gates
Combinational Logic
Sequential Logic
SRAM/ DRAM Cells
18

## Slide 19
Multiplexer
n inputs
log(n) select bits
MUX
Output
19
Given n inputs, choose one based on the select bits.
Example: Given 8 inputs, 3 select bits, choose 1 among them

## Slide 20
Design of a Multiplexer
A
B
A
B
B
A
B
A
X
00
X
01
X
10
X
11
Output
20
inputs
Select bits: A and B
Generate all combinations of select bits
  Only one of the combinations is true.
  For this combination the output of the AND gate is equal to the input (XAB), rest of the outputs of the AND gates are 0
  The output is equal to (XAB OR 0 OR 0 OR 0) = XAB

## Slide 21
Demultiplexer
A
B
A
B
B
A
B
A
Outputs
Input
21
Given 1 input, make it appear on one of n outputs. The output is decided by log(n) select bits

## Slide 22
Working of a Demultiplexer
Same logic
  Generate all combinations of A, B, , and
  Only one combination is TRUE
  The output of that AND gate is equal to: X AND 1 = X Here, X is the input
  The outputs of the rest of the AND gates are 0

## Slide 23
Decoder
A
B
A
B
B
A
B
A
Outputs
23
Set one of the n outputs to 1. The output is decided by log(n) select bits
Operation is similar to a demultiplexer

## Slide 24
Encoder
n inputs
Encoder
log(n) bits
Given n inputs, assume only one of them is 1. Find its id.
For example: if the 6th input out of 8 inputs is 1. The output should be 110

## Slide 25
Example of a 3-bit Encoder
Input bit | Bit2 | Bit1 | Bit0
b0 | 0 | 0 | 0
b1 | 0 | 0 | 1
b2 | 0 | 1 | 0
b3 | 0 | 1 | 1
b4 | 1 | 0 | 0
b5 | 1 | 0 | 1
b6 | 1 | 1 | 0
b7 | 1 | 1 | 1
Bit2 = b4 + b5 + b6 + b7
Output bits
Bit1 = b2 + b3 + b6 + b7
Bit0 = b1 + b3 + b5 + b7
Here, the + symbol stands for OR

## Slide 26
Example of a 3-bit Encoder - II
Bit2
Bit1
Bit0
b4
b5
b6
b7
b2
b3
b6
b7
b1
b3
b5
b7
Outputs
8-bit input

## Slide 27
Outline
Transistors and Gates
Combinational Logic
Sequential Logic
SRAM/ DRAM Cells
27

## Slide 28
28
SR Latch
Q
Q
S
R
S = 1, R = 0, Q = 1
S = 0, R = 1, Q = 0
S = 0, R = 0, <maintain old values>
Use a cross-coupled pair of NAND gates to store a stable value.
Understand these points
Set the values
S  Set
R  Reset

## Slide 29
29
Clocked SR Latch
Q
Q
S
R
Clock
Let us add a clock signal.
  When the clock is 1, outputs of the NAND gates are and respectively (same as the classic SR latch)
  Clock is 0  they are 1 and 1 respectively (maintain old values)

## Slide 30
30
D Flip Flop
Q
Q
D
Clk
D = 1, Q = 1
D = 0, Q = 0
Let us not have two inputs: S and R
Let us consider a single input, D, and modify the clocked SR latched appropriately
If Clk = 1, I1 = , I2 = D  Essentially, this sets Q to D
If Clk = 0, I1 = I2 = 1 (maintain old values)
I1
I2

## Slide 31
31
Master Slave D Flip Flop
D
Clk
Q
Q
Clk
D'
Connect two D flip flops one after the other
Clk
0
Q = D’
1
D’ = D
When the Clk = 1, the value of D gets transferred to the slave (D’)
Then when the Clk transitions to 0 (1  0)
The value of D’ gets transferred to the output (Q)
master
slave
Note the importance of the negative edge

## Slide 32
Master Slave J-K Flip Flop
J
Clk
Q
Q
Clk
master
slave
K
J | K | I1 | I2 | T1 | Clk
0 | 0 | 1 | 1 | Q | 1
1 | 0 | Q | 1 | 1 | 1
0 | 1 | 1 |  | 0 | 1
1 | 1 | Q |  |  | 1
J | K | I1 | I2 | T1 | Clk
0 | 0 | 1 | 1 | Q | 1
1 | 0 | Q | 1 | 1 | 1
0 | 1 | 1 |  | 0 | 1
1 | 1 | Q |  |  | 1
T1
J | K | T1 | Clk | Q
0 | 0 | old Q | 0 | old Q
1 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 0
1 | 1 |  | 0 | 
J | K | T1 | Clk | Q
0 | 0 | old Q | 0 | old Q
1 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 0
1 | 1 |  | 0 | 
I1
I2
Transfer the input to the output
slave is active
master is active
Maintain, Set, Reset, or Toggle

## Slide 33
Outline
Transistors and Gates
Combinational Logic
Sequential Logic
SRAM/ DRAM Cells
33

## Slide 34
SRAM Cell
We want to reduce the number of transistors required to store a single bit
Instead of using a cross-coupled pair of NAND gates, use a cross coupled pair of inverters
A pair of inverters stores 1 bit
Problems: Need extra circuitry to read and write values

## Slide 35
35
SRAM Cell
v
dd
Word line (WL)
BL
BL
(Bit line)
W1
W2
cross coupled
pair of inverters

## Slide 36
SRAM Cell (Alternative Reprsentation)
BL
BL
W1
W2
The word line signal turns W1 and W2 on
  The inverter pair gets connected to the bit lines
Read mode:
  The values of BL and are set to V and respectively. The bit lines are kept floating.
Write mode:
  The values of the terminals, V and are set to the values of BL and respectively. The bit lines are charged by strong driver circuits.
word line
V
Not connected to ground or Vcc
6 Transistor SRAM cell

## Slide 37
37
Array of SRAM Cells
SRAM
cell
SRAM
cell
SRAM
cell
SRAM
cell
SRAM
cell
SRAM
cell
SRAM
cell
SRAM
cell
SRAM
cell
SRAM
cell
SRAM
cell
SRAM
cell
Address
BL
BL
WL
WL
WL
Write
driver
Write
driver
Data in
Sense amplifier
Sense amplifier
Data out
Data in
Column mux/demux
Address
To save space, we arrange SRAM cells into rows and columns
Setting a word line enables all the cells in a row
Only one row can be enabled at a time
D
E
C
O
D
E
R
Use a decoder to set only one word line to 1 (based on the address)
Choose a subset of columns to read or write

## Slide 38
Operating an Array of SRAM Cells
Write mode:
  Use a driver circuit to set the values of BL and
  Simultaneously enable the word line
  The values in BL and will get transferred to the SRAM cell (thus a write)
Read:
  Disconnect the bit lines from supply and ground using transistors (floating)
  Enable the word line
  The values of (BL and ) will get set to logical 1 and 0 respectively if the value stored in the SRAM cell is 1, or vice-versa

## Slide 39
Pre-charging
Issues with the simple design:
  The bit lines are very long, and are connected to a lot of SRAM cells
  They thus have a lot of resistance and capacitance
  Driving them to a logical 0 or 1 (typically 1V) will take a long time
  This will make the SRAM slow
  Can we do something better
Observe:
  Let us pre-charge both the bitlines to 0.5 V (assuming logical 1 is 1V) using strong pre-charge driver circuits
  Let us then enable the word line
  One of the bit lines will move towards 0V and the other towards 1V
  IDEA: Monitor the difference in voltages between the bit lines

## Slide 40
Pre-charging - II
Should we wait for one of the bit lines to reach 0V and the other to reach 1V
  Answer: NO
  If we know the outcome: why wait
Monitor the difference:
  There can be some amount of electrical noise that might cause a little bit of fluctuation in the voltages of the bit line. Define a noise threshold, T.
  The moment: | | > T, declare the result
  If is +ve, infer a logical 1
  Else, infer a logical 0
A very fast method of reading

## Slide 41
41
Array of SRAM Cells
SRAM
cell
SRAM
cell
SRAM
cell
SRAM
cell
SRAM
cell
SRAM
cell
SRAM
cell
SRAM
cell
SRAM
cell
SRAM
cell
SRAM
cell
SRAM
cell
Address
BL
BL
WL
WL
WL
Write
driver
Write
driver
Data in
Sense amplifier
Sense amplifier
Data out
Data in
Column mux/demux
Address
D
E
C
O
D
E
R
Pre-charge
drivers
Write
drivers
Sense amplifiers to monitor the difference in voltages

## Slide 42
42
DRAM Cell (even smaller)
Word line (WL)
BL
(Bit line)
Capacitor is charged  logical 1
No charge across the capacitor  0

## Slide 43
Array of DRAM Cells
Features
  There is a single bit line
  For writing  Enable the word line and charge the bit line with a driver circuit
  For reading  pre charge the bit line to 0.5 V, enable the word line, and monitor the difference of the voltage w.r.t 0.5 V
    If the difference in voltages exceeds a threshold
    Infer a logical 0 or 1 depending on the sign of the difference

## Slide 44
DRAM Refresh
Problems
  After every read, we lose some charge from the capacitor
  Periodically, charge from the capacitor leaks out
  Hence, it is necessary to:
    Periodically read each and every DRAM cell
    And write the same data back
  Example: The charge across the capacitor reduces from 1 V to 0.7 V over time.
    Let’s say, this is enough to infer a logical 1.
    Read the value (logical 1 in this case)
    And write the same value again. We thus restore the charge on the capacitor to 1 V.
This is known as DRAM refresh

## Slide 45
45
Array of DRAM Cells
Decoder
DRAM
cell
DRAM
cell
DRAM
cell
DRAM
cell
DRAM
cell
DRAM
cell
DRAM
cell
DRAM
cell
DRAM
cell
DRAM
cell
DRAM
cell
DRAM
cell
Address
BL
WL
WL
WL
Write
driver
Write
driver
Sense amplifier
Sense Amplifier
Data out
Refresh
Refresh
Data in
Data in
Column mux/demux
Address
Note the refresh circuits
The rest is the same as the SRAM array

## Slide 46
46
CAM Cell
v
dd
Word line (WL)
BL
BL
W1
W2
A
A
match
T1
T2
T3
T4
Instead of enabling cells by their address, can we find them by their contents?
Content Addressable
Memory  CAM
SRAM cell
Content matching circuit
Case: A == V
In the pair (A, ), one of the values has to be 0  Either T3 or T4 is off
Similarly, in the pair (, V), one of the values has to be 0  Either T1 or T2 is off
Thus, match is floating
V
V

## Slide 47
47
CAM Cell
v
dd
Word line (WL)
BL
BL
W1
W2
A
A
match
T1
T2
T3
T4
Instead of enabling cells by their address, can we find them by their contents?
Content Addressable
Memory  CAM
SRAM cell
Content matching circuit
Case: A ≠ V
Either (A, ), or (, V) is equal to (1,1).
This connects the match line to the ground (sets its voltage to 0 volts)
If there is a mismatch, the match line is driven to 0 V
V
V

## Slide 48
48
Array of CAM Cells
Decoder
CAM
cell
Address
BL
BL
Write
driver
Write
driver
Data in
Sense amplifier
Sense amplifier
Data out
Data in
Column mux/demux
Address
A
A
1
1
CAM
cell
CAM
cell
CAM mode
CAM
cell
BL
BL
A
A
2
2
CAM
cell
CAM
cell
CAM
cell
BL
BL
A
A
n
n
CAM
cell
CAM
cell
WL
WL
WL
match
match
Pre-charge all the match lines to 1
If there is a content match, one of the match lines will be 1
The OR gate will thus compute 1 (else 0 if none of the rows match)

## Slide 49
49
Array of CAM Cells - II
Decoder
CAM
cell
Address
BL
BL
Write
driver
Write
driver
Data in
Sense amplifier
Sense amplifier
Data out
Data in
Column mux/demux
Address
A
A
1
1
CAM
cell
CAM
cell
CAM mode
CAM
cell
BL
BL
A
A
2
2
CAM
cell
CAM
cell
CAM
cell
BL
BL
A
A
n
n
CAM
cell
CAM
cell
WL
WL
WL
match
Id of the row
that matched
Use an encoder to find the id of the row that matched.
Encoder

## Slide 50
50
THE END