## Slide 1
Chapter 7 Computer Arithmetic 2
Smruti Ranjan Sarangi, IIT Delhi
Computer Organisation and Architecture
PowerPoint Slides
PROPRIETARY MATERIAL. © 2014 The McGraw-Hill Companies, Inc. All rights reserved. No part of this PowerPoint slide may be displayed, reproduced or distributed in any form or by any means, without the prior written permission of the publisher, or used beyond the limited distribution to teachers and educators permitted by McGraw-Hill for their individual course preparation. PowerPoint Slides are being provided only to authorized professors and instructors for use in preparing for classes using the affiliated textbook. No other use or distribution of this PowerPoint slide is permitted. The PowerPoint slide may not be sold and may not be distributed or be used by any student or any other third party. No part of the slide may be reproduced, displayed or distributed in any form or by any means, electronic or otherwise, without the prior written permission of McGraw Hill Education (India) Private Limited.

## Slide 2
Download the pdf of the book
www.basiccomparch.com
videos
Slides, software, solution manual
Print version
(Publisher: WhiteFalcon, 2021)
Available on e-commerce sites.
The pdf version of the book and all the learning resources can be freely downloaded from the website: www.basiccomparch.com
2nd version

## Slide 3: Outline
Addition
Multiplication
Division
Floating Point Addition
Floating Point Multiplication
Floating Point Division

## Slide 4: Integer Division
Let us only consider positive numbers
  N = DQ + R
    N → Dividend
    D → Divisor
    Q → Quotient
    R → Remainder
Properties
  [Property 1:] R < D, R >= 0
  [Property 2:] Q is the largest positive integer satisfying the equation (N = DQ +R) and Property 1

## Slide 5: Reduction of the Divison Problem
We have reduced the original problem to a smaller problem

## Slide 6: How to Reduce the Problem
We need to find Qn
We can try both values – 0 and 1
  First try 1
  If : N – D2n-1 >= 0, Qn = 1 (maximize the quotient)
    Otherwise it is 0
Once we have reduced the problem
  We can proceed recursively

## Slide 7: Iterative Divider
Initial: V holds the dividend (N), U = 0
U
V
Divisor(D)
(U-D)

## Slide 8: Restoring Division
Algorithm 3: Restoring algorithm to divide two 32 bit numbers
Data: Divisor in D, Dividend in V, U = 0
Result: U contains the remainder (lower 32 bits), and V contains the quotient
i ← 0
for i < 32 do
i ← i + 1
/* Left shift UV by 1 position */
UV ← UV << 1
U ← U - D
if U ≥ 0 then
q ← 1
end
else
U ← U + D
q ← 0
end
/* Set the quotient bit */
LSB of V ← q
end

## Slide 9: Example
00000
111X
after shift:
end of
iteration:
00000
1110
1
00000
0111
beginning:
U
V
00001
110X
after shift:
end of
iteration:
00001
1100
2
00011
100X
after shift:
end of
iteration:
00000
1001
3
00001
001X
after shift:
end of
iteration:
00001
0010
4
Divisor (D)
0011
Dividend (N)
00111
Remainder(R)
0001
Quotient(Q)
0010

## Slide 10: Restoring Division
Consider each bit of the dividend
Try to subtract the divisor from the U register
  If the subtraction is successful, set the relevant quotient bit to 1
  Else, set the relevant quotient bit to 0
Left shift

## Slide 11: Proof
Let us consider the value stored in UV (ignoring quotient bits)
After the shift (first iteration)
  UV = 2N
After line 5, UV contains
  UV – 2nD = 2N – 2nD = 2 * (N – 2n-1 D)
If (U – D) >= 0
  N' = N – 2n-1D.
  Thus, UV contains 2N'

## Slide 12: Proof - II
If (U – D) < 0
  We know that (N = N')
  Add D to U → Add 2nD to UV
  partial dividend = 2N = 2N'
In both cases
  The partial dividend = 2N'
After 32 iterations
  V will contain the entire quotient

## Slide 13: Proof - III
At the end, UV = 232 * N32 (Ni is the partial dividend after the ith iteration)
N31 = DQ1 + R
  N31 – DQ1 = N32 = R
Thus, U contains the remainder (R)

## Slide 14: Time Complexity
n iterations
  Each iteration takes log(n) time
  Total time : n log(n)

## Slide 15: Restoring vs Non-Restoring Division
We need to restore the value of register U
  Requires an extra addition or a register move
Can we do without this ?
  Non Restoring Division

## Slide 16
Algorithm 4: Non-restoring algorithm to divide two 32 bit numbers
Data: Divisor in D, Dividend in V, U = 0
Result: U contains the remainder (lower 32 bits), and V contains the quotient
i ← 0
for i < 32 do
i ← i + 1
/* Left shift UV by 1 position */
UV ← UV << 1
if U ≥ 0 then
U ← U − D
end
else
U ← U + D
end
if U ≥ 0 then
q ← 1
end
else
q ← 0
end
/* Set the quotient bit */
lsb of V ← q
end
if U <0 then
U ← U + D
end

## Slide 17
00000
111X
after shift:
end of
iteration:
11101
1110
1
00000
0111
beginning:
U
V
11011
110X
after shift:
end of
iteration:
11110
1100
2
11101
100X
after shift:
end of
iteration:
00000
1001
3
00001
001X
after shift:
end of
iteration:
11110
0010
4
Divisor (D)
0011
Dividend (N)
00111
Remainder(R)
0001
Quotient(Q)
0010
0001
0010
end (U=U+D):
U
V

## Slide 18: Idea of the Proof
Start from the beginning : If (U – D) >= 0
  Both the algorithms (restoring and non-restoring) produce the same result, and have the same state
If (U – D) < 0
  We have a divergence
  In the restoring algorithm
    value(UV) = A
  In the non-restoring algorithm
    value(UV) = A - 2nD

## Slide 19: Proof - II
In the next iteration (just after the shift)
  Restoring : value(UV) = 2A
  Non - Restoring : value(UV) = 2A - 2n+1D
If the quotient bit is 1 (end of iteration)
  Restoring :
    Subtract 2nD
    value(UV) = 2A - 2nD
  Non Restoring :
    Add 2nD
    value(UV) = 2A – 2n+1D + 2nD = 2A - 2nD

## Slide 20: Proof - III
If the quotient bit is 0
  Restoring
    partial dividend = 2A
  Non restoring
    partial dividend = 2A – 2nD
  Next iteration (if quotient bit = 1) (after shift)
    Restoring : partial dividend : 4A
    Non restoring : partial dividend : 4A – 2n+1D
Keep applying the same logic ….

## Slide 21: Outline
Addition
Multiplication
Division
Floating Point Addition
Floating Point Multiplication
Floating Point Division

## Slide 22: Adding Two Numbers (same sign)
Recap : Floating Point Number System
Normalised form of a 32 bit (normal) floating point number.
Normalised form of a 32 bit (denormal) floating point number.
A = (−1)S × P × 2−126, (0 ≤ P < 1) (7.23)
Symbol
Meaning
S
Sign bit (0(+ve), 1(-ve))
P
Significand (form: 1.xxx(normal) or 0.xxx(denormal))
M
Mantissa (fractional part of significand)
E
(exponent + 127(bias))
Z
Set of integers
A = (−1)S × P × 2E−bias, (1 ≤ P < 2, E ∈ Z, 1 ≤ E ≤ 254) (7.22)

## Slide 23: Addition
Add : A + B
  Unpack the E fields → EA , EB
  Let the E field of the result be → EC
Unpack the significand (P)
  P contains → 1 bit before the decimal point, 23 mantissa bits (24 bits)
  Unpack to a 25 bit number (unsigned)
    W → Add a leading 0 bit, 24 bits of the signficand

## Slide 24: Addition - II
With no loss of generality
  Assume EA >= EB
Let significands of A and B be PA and PB
Let us initially set W ← unpack (PB)
We make their exponents equal and shift W to the right by (EA – EB) positions

## Slide 25: Renormalisation
Let the significand represented by register, W, be PW
  There is a possibility that PW >= 2
  In this case, we need to renormalise
    W ← W >> 1
    EA ← EA + 1
The final result
  Sign bit (same as sign of A or B)
  Significand (PW), exponent field (EA)

## Slide 26: Example
Example: Add the numbers: 1.012 * 23 + 1.112 * 21
Answer:
The decimal point in W is shown for enhancing readability. For simplicity, biased notation not used.
A = 1.01 * 23 and B = 1.11 * 21
W = 01.11 (significand of B)
E = 3
W = 01.11 >> (3-1) = 00.0111
W + PA = 00.0111 + 01.0100 = 01.1011
Result: C = 1.011 * 23

## Slide 27: Example - II
Example: Add : 1.012 * 23 + 1.112 * 22
Answer:
The decimal point in W is shown for enhancing readability. For simplicity, biased notation not used.
A = 1.01 * 23 and B = 1.11 * 22
W = 01.11 (significand of B)
E = 3
W = 01.11 >> (3-2) = 00.111
W + PA = 00.111 + 01.0100 = 10.001
Normalisation: W = 10.001 >> 1 = 1.0001, E = 4
Result: C = 1.0001 * 24

## Slide 28: Rounding
Assume that we were allowed only two mantissa bits in the previous example
  We need to perform rounding
Terminology :
  Consider the sum(W) of the significands after we have normalised the result
  W ← (P + R) * 2-23 (R < 1)

## Slide 29: Rounding - II
P represents the significand of the temporary result
R (is a residue)
Aim :
  Modify P to take into account the value of R
  Then, discard R
  Process of rounding : P → P'

## Slide 30: IEEE 754 Rounding Modes
Truncation
  P' = P
  Example in decimal : 9.5 → 9, 9.6 → 9
Round to +∞
  P' = ⎡P +R⎤
  Example in decimal : 9.5 → 10, -3.2 → -3

## Slide 31: IEEE 754 Rounding - II
Round to -∞
  P' = ⌊P+R⌋
  Example in decimal : 9.5 → 9, -3.2 → -4
Round to nearest
  P' = [P + R]
  Example in decimal :
    9.4 → 9 , 9.5 → 10 (even)
    9.6 → 10 , -2.3 → -2
    -3.5 → -4 (even)

## Slide 32: Rounding Modes – Summary
Rounding Mode
Condition for incrementing the significand
Sign of the result (+ve)
Sign of the result (-ve)
Truncation
Round to +∞
Round to −∞
Round to Nearest
R > 0
(R > 0.5)||(R = 0.5 ∧ lsb(P) = 1)
R > 0
(R > 0.5)||(R = 0.5 ∧ lsb(P) = 1)
∧ (logical AND), R (residue)

## Slide 33: Implementing Rounding
We need three bits
  lsb(P)
  msb of the residue (R) → r (round bit)
  OR of the rest of the bits of the residue (R) → s (sticky bit)
Condition on Residue
Implementation
R > 0
R = 0.5
R > 0.5
r ∨ s = 1
r ∧ s = 1
r ∧ s = 1
r (round bit), s(sticky bit)

## Slide 34: Renormalisation after Rounding
In rounding : we might increment the significand
  We might need to renormalise
  After renormalisation
    Possible that E becomes equal to 255
    In this, case declare an overflow

## Slide 35: Addition of Numbers (Opposite Signs)
C = A + B
  Same assumption EA >= EB
Steps
  Load W with the significand of B (PB)
  Take the 2's complement of W (W = -B)
  W ← W >> (EA – EB)
  W ← W + PA
  If (W < 0) replace it with its 2's complement. Flip the sign of the result.

## Slide 36: Addition of Numbers (Opposite Signs)-II
Normalise the result
  Possible that W < 1
  In this case, keep shifting W to the left till it is in normal form. (simultaneously decrement EA)
Round and Renormalise

## Slide 37
A=0?
C=B
B=0?
C=A
Y
Y
N
sign(A) = sign(B)?
Swap A and B
such that E <= E
A
B
W
P >> (EA – EB)
Y
N
W
W + P
W
- W (2's complement)
Normalize W and
update E
Round W
B
A
E
E
A
, S
sign(A)
N
W < 0?
W
- W (2's complement)
S = S
Y
N
Normalize W and
update E
Overflow or
underflow?
Overflow or
underflow?
N
N
Report
Y
Report
Y
Construct C out
of W, E, and S
C
C = A + B

## Slide 38: Outline
Addition
Multiplication
Division
Floating Point Addition
Floating Point Multiplication
Floating Point Division

## Slide 39: Multiplication of FP Numbers
Steps
  E ← EA + EB - bias
  W ← PA * PB
  Normalise (shift left or shift right)
  Round
  Renormalise

## Slide 40
A=0?
C=0
B=0?
C=0
Y
Y
N
Normalize W and
update E
Round W
E
E + E - bias
A
sign(A) sign(B)
N
Normalize W and
update E
Overflow or
underflow?
Overflow or
underflow?
N
N
Report
Y
Construct C out
of W, E, and S
C
C = A * B
S
B
Overflow or
underflow?
Report
Y
P
A
W
P
B
*
N
Report
Y

## Slide 41: Outline
Addition
Multiplication
Division
Floating Point Addition
Floating Point Multiplication
Floating Point Division

## Slide 42: Simple Division Algorithm
Divide A/B to produce C
  There is no notion of a remainder in FP division
Algorithm
  E ← EA – EB + bias
  W ← PA / PB
  normalise, round, renormalise
Complexity : O(n log(n))

## Slide 43: Goldschmidt Division
Let us compute the reciprocal of B (1/B)
  Then, we can use the standard floating point multiplication algorithm
Ignoring the exponent
  Let us compute (1/PB)
If B is a normal floating point number
  1 <= PB < 2
  PB = 1 + X (X < 1)

## Slide 44: Goldschmidt Division - II

## Slide 45
No point considering Y32
Cannot be represented in our format

## Slide 46: Generating the 1/(1-Y)
We can compute Y2 using a FP multiplier.
  Again square it to obtain Y4, Y8, and Y16
  Takes 4 multiplications, and 5 additions, to generate all the terms
  Need 4 more multiplications to generate the final result (1/1-Y)
Compute 1/PB by a single right shift

## Slide 47: GoldSchmidt Division Summary
Time complexity of finding the reciprocal
  (log(n))2
Time required for all the multiplications and additions
  (log(n))2
Total Time : (log(n))2

## Slide 48: Division using the Newton Raphson Method
Let us focus on just finding the reciprocal of a number
Let us designate PB as b (1 <= b < 2)
  Aim is to compute 1/b
Let us create a function f(x) = 1/x – b
  f(x) = 0, when x = 1/b
Problem of computing the reciprocal
  same as computing the root of f(x)

## Slide 49: Idea of the Method
Start with an arbitrary value of x → x0
  Locate x0 on the graph of f(x)
  Draw a tangent to f(x) at (x0 , f(x0))
  Let the tangent intersect the x axis at x1
  Draw another tangent at (x2, f(x2))
Keep repeating
  Ultimately, we will converge to the root

## Slide 50: Newton Raphson Method
x0
x0,f(x0)
x1
x2
root
x
f(x)
x1,f(x1)

## Slide 51: Analysis
f(x) = 1/x – b
  f’(x)= d f(x) / d(x) = -1 / x2
  f'(x0) = -1/x02
Equation of the tangent : y = mx + c
  m = -1/x02
  y = -x/x02 + c
At x0, y = 1/x0 - b

## Slide 52: Algebra
The equation of the tangent is :
  y = -x/x02 + 2/x0 – b
  Let this intersect the x axis at x1

## Slide 53: Intersection with the x-axis
Let us define : E(x) = bx – 1
  E(x) = 0, when x = 1/b

## Slide 54: Evolution of the Error

## Slide 55: Bounding the Error
1 <= b < 2 (significand of a normal floating point number)
  Let x0 = ½
  The range of (bx0 – 1) is [-1/2, 0]
  Hence, |E(x0)| <= ½
  The error thus reduces by a power of 2 every iteration

## Slide 56: Evolution of the Error - II
E(x) = bx – 1 = b (x – 1/b)
  x – 1/b is the difference between the ideal value and the actual estimate (x). This is near 2-32, which is too small to be considered.
No point considering beyond 5 iterations
Since, we are limited to 23 bit mantissas
Iteration
max(e (x)
0
1
2
1
1
2
2
2
1
2
4
3
1
2
8
4
1
2
16
5
1
2
32

## Slide 57: Time Complexity
In every step, the operation that we need to perform is :
  xn = 2xn-1 – bxn-12
  Requires a shift, multiply, and subtract operation
  O(log(n)) time
Number of steps: O(log(n))
Total time : O( log (n)2 )

## Slide 58
THE END