## Slide 1: Energy Efficient Scheduling in IoT Networks
Smruti R. Sarangi, Sakshi Goel, Bhumika Singh
Indian Institute of Technology Delhi

## Slide 2: Projections regarding IoT Networks
50-100 billion devices
450 billion $ market
Smart cities, Industrial IoT, Connected health
Forbes Forecasts [1]

## Slide 3: Major Challenge in IoT Networks: Energy Efficiency
Most IoT nodes run on batteries
Many use intermittent sources of power
Many applications need real time data analytics support

## Slide 4: More about Energy Dissipation
We only focus on computation energy (up to 99% of energy consumption)
Existing methods: DVFS, throttling, low power states
Processor
Communication
Energy
Computation
Energy

## Slide 5: Problems with Current Approaches
They make local choices
The choice is independent of
  State of the environment
  Actions of other nodes
Can we coordinate energy reduction mechanisms between IoT nodes?
Will it lead to benefits?

## Slide 6: Typical IoT Stack
Region of Interest

## Slide 7: Relevant Background
A  Activity factor
P  power
C  capacitance
V  voltage
f  frequency
Reduce the activity
Reduce the voltage and frequency (DVFS)
Reduce both

## Slide 8: Reducing Energy Consumption in Sensor Networks
Duty Cycling
Data Driven Approaches
Mobility Driven Approaches
Power the nodes off when they do not need to sense a signal or they do not need to transmit
Change the sampling rate,
data quantization, and
eliminate redundancy
Move the motes closer to the
source of the signal

## Slide 9: Model of the System
Sensors  Smart Gateways  Cloud
From the sensors
to the cloud
From the cloud to
the actuators

## Slide 10: Problem Statement
AIM: For a task minimize the energy without missing the deadline.
Approach:
  At each node keep a dynamic estimate of the time required to finish the task
  Perform DVFS at each node accordingly
  Assume each node is a multicore processor, where we can set different frequencies per core
Task
Start time
Deadline
Network Traffic (bytes)
Worst case exec. cycles at each node

## Slide 11: Algorithm for Applying DVFS at each Node
trem  max_time_to_execute_task()
if (trem ≤ 0) run any core at freqmax ; return
if (there is an idle core)
run on idle core with frequency = C/ trem
else
run on a core with min. frequency fi such that wi + ci/fi ≤ trem
if no such core found 
increase frequency of core with maximum frequency to freqmax
`
freqmax  maximum frequency
C  Total exec. cycles
wi  average waiting time
Periodically reduce the frequency of high frequency cores

## Slide 12: Main Problem
We need to have a good estimate of test
Then only we can compute trem = deadline – current_time - test
sensor
actuator
Gateways
Task
test

## Slide 13: Global Algorithm
Each node computes a tavg  average time between job arrival and departure
It periodically sends it to the CS
Separate tavg computed for each predecessor
sensor
actuator
Gateways
Central Server (CS)
CS
tavg for each predecessor
Node
Pred
tavg

## Slide 14: Global Algorithm - II
The server computes test
  Sum of the tavg values for all the nodes in the chain till the actuator
  Plus the worst case network latency across all hops
Enhancements
Maintain a moving average of tavg values
Use a distribution instead of a single value.

## Slide 15: Local Algorithm
Every node maintains a table of test values for its neighbors
The test is piggybacked with every message
Additionally, nodes often share this value with their neighbors (1 or 2 hop distance)
Nodes add or subtract tavg, to update test depending on the direction
They maintain a weighted moving average of test
test
Task
test

## Slide 16: Stability Properties
Assume we initialize the system with the correct values of tavg and test
  It will remain stable
If there are perturbations in the compute time or network delay
  They will get conveyed from the source of the perturbation to its neighbors.
  The information will gradually propagate
Nodes near the actuator will always have accurate values.
  They will send this downstream

## Slide 17
Evaluation

## Slide 18: Simulation Setup
IoT Simulator
Validated with NS3
and CloudSim
Real World IoT Data
Sinaeepourfard et al.
Data for Barcelona City
Configurations
No-DVFS
Deadline-Share
Gateway
Server
DVFS Step
0.5-1 GHz
1.5-2 GHz
100 MHz
1. 64 bit Ubuntu Linux System
Intel Core i7 CPU, 3.10 Ghz, 4 GB RAM
2. Energy values taken from the Tejas architectural simulator

## Slide 19: Deadlines
Number of Sensors | Tight Deadlines | Loose Deadlines
16 | 3-4% | 9-12%
32 | 4-6% | 14-18%
64 | 7-10% | 23-28%
128 | 13-15% | 40-45%
256 | 22-26% | 69-76%
512 | 40-44% | 80-90%
1024 | 72-78% | 95-100%

## Slide 20
Energy Minimization with Tight Deadlines
Local does not scale
Mostly as good as global
Baseline:
No-DVFS

## Slide 21
Energy Minimization with Tight Deadlines
Energy Minimization with Tight Deadlines
Baseline:
Deadline-Share
30-50% task
drops for deadline-share

## Slide 22
Energy Minimization with Loose Deadlines
Baseline:
Deadline-Share
30-50% task drops
with Deadline-Share

## Slide 23: Frequency of Sensing
Sensing Interval (s)
% Deadlines Violated

## Slide 24: Task Drop Rates

## Slide 25: Conclusions
Co-operative protocols can yield significant energy savings in IoT networks
The global algorithm is the best in terms of scalability and task drop rates
  It is hard to implement
The gossip based local algorithm performs very well for small and medium loads
  It has scalability issues.
The search is on for a good hybrid approach ....

## Slide 26: References
https://www.forbes.com/sites/louiscolumbus/2017/12/10/2017-roundup-of-internet-of-things-forecasts